## Slide 1: Optical Wireless Communication – Trade-off between different parameters – Part I
z.ghassemlooy@northumbria.ac.uk
Dec. 2024
Prof Zabih Ghassemlooy, Northumbria University, UK
Prof Stanislav Zvanovec, Czech Technical University in Prague, Czech Republic
Dr Luis Nero Alves, Uinsti. De Telec., University of Aveiro, Portugal
Dr Ali Khalighi, Ecole Centrale Marseille, Institut Fresnel, France
Dr Mónica J C de Figueiredo, Politécnico de Leiria, Portugal
Dr Anna Maria Vegni, Università degli Studi Roma Tre, Italy
Dr Joaquin Perez Soler, Universitat de València, Spain
Dr Xicong Li, Northumbria University, UK
Prof Hoa Le-Minh, Northumbria University, UK

## Slide 2: Introduction
A system is a complex entity to deal with it, where there are so many parameters needs to be considered to achieve the required performance metrics. This process also involves trade-off between many different parameters and performance metrics. This set of slides outlines some of the key modules and their features in optical wireless communication systems, as well as the key performance indicators. It is by no means a complete overview but is a starter that could be beneficial to MSc and PhD students doing research in optical wireless communications, which can also be applied to other communications with some changes.
Any comments, suggestions, etc. are welcome.
Z. Ghassemlooy

## Slide 3
Communication System
Transmitter (Tx)
Channel
Receiver (Rx)
Noise
+
Interference
x(t)
r(t)
n(t)
d(t)
C. -X. Wang, J. Huang, H. Wang, X. Gao, X. You and Y. Hao, "6G Wireless Channel Measurements and Models: Trends and Challenges," in IEEE Vehicular Technology Magazine, vol. 15, no. 4, pp. 22-32, Dec. 2020, doi: 10.1109/MVT.2020.3018436.
Channel capacity
Csum:
B
P
No. of channels (space/time/frequenc)
No. of HetNets
Interference
Noise

## Slide 4
Spectral efficiency
&
Energy efficiency
Bandwidth
&
throughput
RSSI
SNR/SNIR
PNR
ENR
Linearity
&
dynamic range
KPIs
Latency
&
Jitter
Power & rise time (bandwidth) budgets
Complexity
&
costs
Data rates
Eye & constellation diagrams
&
EVM
BER
SER
PER
Outage Prob.
Interference
Metrics - Ways to measure the performance of communication systems and provide a clear picture of network performance.
How to use metrics?
  Measure the actual performance of real systems
  Calculate/estimate to predict performance of planned systems
Represented using different statistics
  Instantaneous
  Average (mean) over some time
  Maximum (peak)
  Minimum,
  Standard deviation
  Variance, . . .
Performance Metrics
Z. Ghassemlooy
Standards
Connectivity
density
Coverage
& mobility

## Slide 5
BER
Is a function of the type of:
  Modulation
  Characteristics of the modulator and demodulator
  Quality of the transmission channel.
May be affected by:
Order of modulations
  Lower order modulation but at the cost of data throughput.
Transmit power Pt
Transmission channel
  attenuation
  multipath fading
  noise
Bandwidth B
Interference I
Distortion
Bit synchronization problems
etc.
E.g., OOK-NRZ
)
BER =
)
K: Information bits  to the encoder/modulator
Message energy
Z. Ghassemlooy
The challenge is to achieve low BERs at low Eb/No or S/N levels.

## Slide 6
Physical Layer
Channel
Rx
LED/LD
Tx mode
Lense
&
Beamforming
Single or multiple
Types and beam profiles
Cells size and density
Field of view
Wavelength
Maximum current Imax
Voltage Vmin & Vmax
Power out (illumination) Po
Po vs. I plot
  Dynamic range
  Non-linearity
Bandwidth BLED
DC-biasing
Diversity
Equ.
LOS
NLOS
Diffused
Loss
Dispersion
Type
Bandwidth
Power usage
Type
Size
Power loss
Beam size and minimum Pt
Complexity
Data
Mux
Noise
Interference
KPI
Mod
Coding
Types
Efficiency
BER, ENR and SNR
Complexity
Z. Ghassemlooy
Amp
Types
Efficiency
Gain
Linearity
Format
Pulse shaping
Bandwidth
Power (avg, max)
Synch
Tx
Type (single & multilevel)
Bandwidth - optimized to use available frequency spectrum
Mod. Index
Encryption and error correction
Adaptable
Power (avg, max)
Pmin to deliver SNR
Synch.

## Slide 7
Physical Layer
Tx
Channel
Rx
Indoor/outdoor
Length
LOS
NLOS
Transfer function
Bandwidth (capacity
Losses
Fading
Dispersion
Static/dynamic
Shadowing/blocking
Conditions: Fog, rain, turbulence, etc.
Others
Noise
Interference
Types and sources
  Shot noise
    Signal depen,
    Ambient light
  Dark current noise
  Thermal noise
  Amplifier noise
  Noise in IS-based Rx
PSD
Standard deviation
Dominant noise
Lense
PD/APD/IS/PV
  Type and size
  Field of view
  Responsivity (minimum power)
  Power vs. current charac.
  Bandwidth
Amplifier
  Type
  Gain and linearity
  Bandwidth
Decoding/Demultiplexing/Demodulation
Detection schemes
  Hard/soft (slicing, MF, etc.)
  Processing time
Diversity
Equalizer
Synchronization
Power usage
Type
Sources
KPI
Z. Ghassemlooy

## Slide 8
Bandwidth B
  As B  noise  SNR
  But  data throughput + S  SNR  BER
Transmitter power Pt
Pt  SNR  BER
But,
 Interference to other users  SNIR  BER
 Size of the power amplifier + nonlinearity
 Overall power consumption
 Battery life
Overall cost
Z. Ghassemlooy
Some Examples

## Slide 9
Interference I
Generally, this is set by external factors and cannot be changed by the system design.
More problematic in frequency/wavelength multiplexing-based systems
  Due to:
    Competing wireless devices
    Time/frequency/wavelength reuse
Can be reduced by:
Guard bands between channels  Bandwidth for data  Data throughput
Better filtering  Complexity
Lower system bandwidth  data rate
Lower Pt  SNR  BER
Multiuser detection and spread spectrum  Complexity
Directional antennas  Complexity
Dynamic channel allocation  Complexity
Z. Ghassemlooy
Some Examples
Can lead to several issues::
Reduced signal power  SNR  BER
Dropped connections  Delayed downloads
Network slowdown - Reduced coverage and capacity

## Slide 10
How to achieve the required BER performance
E.g., a BER of 10-6, for high-quality data communications
BER: 10-6
SNR or ENR
S or E
N
I
B/W
Filtering
Rx
Eng
Non-lin.
Har. Dis.
BER
Costly
devices
If too low
 S or E
BER
SNR or ENR
Not the best option
Mod. Type
Complexity
Not what we wanted
Not what we wanted
If too narrow
 S or E
Z. Ghassemlooy
Some Examples

## Slide 11: Coding/Decoding
Efficient use of bandwidth
Tolerance to noise  Improved ENR and SNR  BER
BER vs coding type
Complexity and cost
Standards
Trade-off between error detection and correction capabilities – Depends on the specific application.
  In applications where:
    Error detection – High code rates such as convolutional codes.
    Error correcting – Lower code rates such as:
      Turbo codes
      Low-density parity-check codes
      Concatenated codes.
Z. Ghassemlooy
Some Examples

## Slide 12
Monitor Systems
Problems might be originated from either devices or from modules.
Some common issues are:
Hardware incompatibility
Impedance mismatch
Configuration error
Lack of bandwidth
Saturation or cut-off
Phase delay
Operating outside a dynamic range
etc
Investigate Root Causes
Fix Problem
Identify Problems
Z. Ghassemlooy

## Slide 13
Thank you!
Z. Ghassemlooy